Instrument: the CAN bus communication specification

1. Communication specifications

The data link layer principles should be followed

Bus rate: 250kbps

For the data link layer regulations, please reference the relevant regulations of the CAN2.0 B and J1939.

Each component of the CAN bus has a terminal resistor (120 ohms).

All nodes of the CAN bus are light-coupler isolation, and all the bus driver chips are the PHILIPS 82C250.

Sending cycle 40ms, 2 frames, each frame 20ms.

Use CAN expand frame 29th identifier

The first frame ID code is 0x10088A9E. Data is as follows:

| DATA |
| --- |
| LOCATION | DATA NAME | Explain |
| BYTE1 | voltage low byte | 0.1V/bit offset：-10000 range：0 V～500V |
| BYTE2 | voltage high byte |  |
| BYTE3 | current low byte | 0.1A/bit offset：-10000； current range：-500A～500A |
| BYTE4 | current high byte |  |
| BYTE5 | controller temperature | 1℃/bit offset：40℃ limits：0℃～100℃ |
| BYTE6 | running state | See attachment |
| BYTE7 | fault code low byte | See attachment |
| BYTE8 | fault code high byte |  |

Running status explanation:：

| BIT7 | BIT6 | BIT5 | BIT4 | BIT3 | BIT2 | BIT1 | BIT0 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| reserved | Ready for | reserved | reserved | stop | brake | backward | forward |

Fault code instructions: below are the low bytes, no meaning for the high bytes now.

| BIT7 | BIT6 | BIT5 | BIT4 | BIT3 | BIT2 | BIT1 | BIT0 |
| --- | --- | --- | --- | --- | --- | --- | --- |
| 0 | ERR7 | ERR6 | ERR5 | ERR4 | ERR3 | ERR2 | ERR1 |
| 75 ℃ | BMS | Over speed | Over heating | Over voltage | Under voltage | Over current | IGBT |

The second frame ID code is 0x10098A9E. Data is as follows:

| DATA |
| --- |
| LOCATION | DATA NAME | explain |
| BYTE1 | motor speed low byte | 1rpm offset： 0 range：0 ～10000 |
| BYTE2 | motor speed high byte |  |
| BYTE3 | mileage low byte | kilometer offset：0； range：0～30000 |
| BYTE4 | mileage high byte |  |
| BYTE5 | motor torque low byte | 0.1NM offset：-10000 range：-1000～1000 |
| BYTE6 | motor torque high byte |  |
| BYTE7 | reserved |  |
| BYTE8 | reserved |  |