##### EV MOTOR DRIVE SYSTEM

USER’S MANUAL

Copyright© Shenzhen Great Land Electrics Co., Ltd.

This product is designed for EV drive system，including two parts of motor and controller.

This manual consists of much more information such as system structure, specifications, wiring, circuit diagram, installation, trouble shooting, system maintenance and communication protocol etc.

Please read through this manual for correct operation and we suggest you keep it on hand after reading for future reference.

Please notify us promptly and don’t open and repair controller and motor yourself when you find any trouble with the system. Or else we have no responsibility for you.

We will reserve rights to make improvements and changes in this manual at any time without notice.

- System Introduction

- Wiring

- Circuit Diagram

- Mounting

- Communication Protocol

- Protective Functions

- Maintenance

- Troubles and Solutions

Appendix A: Product Specifications

Appendix B: Motor Outline and Dimensions

Appendix C: Controller Outline and Dimensions

This system consists of motor and controller introduced as follows.

1.1 Motor

In this system PM motor is cooled by water and made of the following parts.

1.1.1 Stator

Stator comprises of casing and winding core.

1.1.2 Rotor

Rotor consists of rotor shaft and permanent magnet block core.

1.1.3 covers

Front cover is of a spigot for installation and rear cover has tapped holes for installation of speed sensor. There are high-quality deep-groove sealed and self oiling bearings in the front cover and the rear cover.

1.1.4 Speed sensor and protective cover

Speed sensor located on the rear end of the motor is kept from damage by protective cover. Its stator is fixed on the rear end-cover and its rotor is fixed on the motor shaft.

1.1.5 Three-phase lead-out cables

Three-phase lead-out cables is connected with the motor stator windings respectively and kept in connection with the cables of the controller by the same color mark at the terminal of each cable during working.

1.1.6 Motor serial number

Only one serial number is allocated to each motor and stamped on the fin of the motor casing, shown in the follow picture.

1.2 Controller

In the system controller cooled by water comprises the following parts.

1.2.1 Radiator

Radiator consists of aluminum heatsink and water channel parts.

1.2.2 Housing

The housing made of bended steel sheet keeps the electrical components from damage and its surface is painted with powder.

1.2.3 Main circuit

Main circuit consists of power device, electrolysis capacitors and absorption capacitors.

1.2.4 Lead-out signal wires

The lead-out signal wires of the controller are used for communication with outer device.

1.2.5 Controller serial number

Only one serial number is allocated to each controller and stamped on the edge of the heatsink, shown in the follow picture.

2.1 For 288V 40kW (for reference only)

4.1  About motor

You can mount motor on the chassis of vehicle through 4 threaded holes in front cover and 4 threaded holes in rear cover with long bolts. And there is an external spigot on the front cover for fixing the motor to connecting plate or gear box. The torque is transmitted by joining the shaft of motor with the shaft of gear box.

You should keep enough space and a well-ventilated area for the natural air-cooled motor from damage.

4.2  About controller

- Keep the area around controller clean and dry. Avoid direct exposure to high temperature, wet environment, sunlight and corrosive air.

- Fix the controller on a level frame through four holes in the heatsink and add cushion for a vibratory place.

- Keep an ambient temperature of below 45ºC.

We use serial communications interface (SCI) in the controller for communication and send the state information of controller timely. You can also select CAN (controller area network) for communication as need.

We have some protective functions for the controller, described as follows.

| function | description |
| --- | --- |
| Power modules fault | Once the power modules detect overcurrent or overheat, the controller will close off any output and give an alarm, and switch off the main contactor. You can recover the system running by turning key switch to “on” position to reset the system. If this arises repetitively, it is regarded as a fault. |
| Overcurrent | Once the circuit detects the output current is greater than the set value, the controller will close off any output and give an alarm，and switch off the main contactor. You can recover the system running by turning key switch to “on” position to reset the system. If this arises repetitively, it is regarded as a fault. |
| Overvoltage | When the voltage of DC bus is over max. allowed value during brake or in any term, the controller will close off any output and give an alarm. You can recover the system running by turning key switch to “on” position to reset the system. If this arises repetitively, it is regarded as a fault. |
| Electronic thermal sensitive relay | Electronic thermal sensitive relay for motor overload makes an inverse proportion between time and load. It will keep an accumulation of repeated heat, and will ignore the heat arising contingently. It will give an alarm for motor overload instead of closing off the controller output. |
| Undervoltage | When the voltage of battery is under the low voltage threshold (this value is adjustable as you need), the controller will close off any output and give an alarm. |
| overheat | When the temperature of the heatsink is over 45ºC, the fans begin to work. When it is below 40ºC, the fans will be switched off. And when it is over 75ºC, the controller will give an alarm and decrease the output torque by a half, when it is still up to 85ºC, the controller will close off any output and give an alarm. The system will work again when the temperature drop to 70ºC after the half torque reduced. |
| Top motor speed | When motor speed is up to the top value, the controller will reduce the torque output. When the speed is still up to 6500rpm, the controller will close off any output. |
| Throttle pedal | An output of throttle potentiometer arises while power on the system, the controller will close off any output. |

7.1  About motor

- Clean dust and smear on the surface of motor periodically.

- Please trained technician to replace jacket of the lead-out cables of motor if necessary.

7.2  About controller

- Don’t wash the controller in spite of the water-proof design.

- Don’t open the cover of controller unless necessary indeed.

- Clean dust and smear on the surface of controller periodically.

- Don’t test the control circuit with high-resistance meter.

- Begin to maintain, repair and reconnect the cables after one minute power off, and protect you from electrical shock or damage components of the controller.

8.1  About motor

8.1.1  Insulating resistance to ground

Insulating resistance to ground of motor in our factory is great than or equal to 20MΩ. It will be less than 2 MΩ when the motor is wetted，you should dry the motor before using it again.

8.1.2 hard to startup

Check mechanical and electrical parameters of the motor step by step, it is only permitted to break down and install motor by trained technician if necessary.

- The motor can not run at absence of phase.

8.2 About controller

Here are some troubles, possible causes and solutions, described as follows.

| trouble | possible causes | solutions |
| --- | --- | --- |
| over-current or power device defect | power device breakdown Grounded or shorted at load side. | Exchanged power device by trained technician. Check the cables motor and output cables. |
| unstable running with much noise | abnormal voltage output due to power device breakdown | Exchanged power device by trained technician. |
| no response to power on | Fuse tube onboard breakdown or without precharge. | Replace fuse tube (beside the 16-pin connector). If need, check and replace the resistor and relay for precharge. |
| unable to rotate but wobbling and without protective signal output | improper cables connection | Check and correct cables connection |

A1: Motor parameters (GLMP25L1)

| Parameter | Unit | Value | Parameter | Unit | Value |
| --- | --- | --- | --- | --- | --- |
| Rated power | kW | 40 | Peak torque | N.m | 250 |
| Battery voltage | V | 288 | Sizes | mm | Ф292×276 |
| Nominal speed | rpm | 3150 | Speed range | rpm | 0－5000 |
| Efficiency | % | 95 | Winding connection |  | Y-type |
| Insulation |  | class F | Protection |  | IP54 |
| Cooling |  | coolant | Weight | kg | 88 |

A2: Controller parameters (GLCP7024L11)

| parameter | unit | value | parameter | unit | value |
| --- | --- | --- | --- | --- | --- |
| Max. capacity | kVA | 100 | Input voltage | DCV | 288 |
| Output voltage | V | 168 | Current rating | A | 105 |
| Ambient temperature | ℃ | -20-60 | Peak current | A | 330 |
| efficiency | % | 95 | Protection |  | IP54 |
| Cooling |  | coolant | weight | kg | 11.0 |

A3: System parameters

| parameter | unit | value | description |
| --- | --- | --- | --- |
| Input voltage | DCV | 288 | Allowed value is 200~400 Vdc，but lower voltage will bring about poor ability. |
| Rated torque | N.m | 127 | Running in long-time |
| Max. torque | N.m | 250 | running time is about 1minute |
| Peak power | kW | 80 |  |
| Top speed | rpm | 5000 | Adjustable by user |
| Speed range | rpm | 0－5000 |  |
| Torque controlled by |  |  | Throttle pedal |
| Control strategy |  |  | Space vector |
| Communication interface |  |  | SPI (CAN optional) |
| Energy regen |  |  | Adjusted as need |
| Protection function |  |  | Overvoltage, overcurrent, power device default, undervoltage, overload and overheat etc. |
| Speed sensor |  |  | Position sensor，power supply 5VDC |

# Text boxes

Company: Shenzhen Great Land Electrics Co., Ltd.

ADD: Floor 6 westside, Block A, Dakan TechnicalGarden Xili,

Nanshan District, Shenzhen, China

Website: www.glelec.com

TEL: 0755—86330861

FAX: 0755—86330856